## Slide 1: Extraction Techniques
By
Dr. Upendra B. Gandagule
HOD
Department of Pharmacognosy
KYDSCT’s College of Pharmacy, Sakegaon

## Slide 2: Counter-current extraction
In Counter-current extraction, wet raw material is pulverized using tooth disc disintegrators to produce a fine slurry.
In his process, the material to be extracted is moved in one direction generally in the form of a fine slurry) within a cylindrical extractor where it comes in contact with extraction solvent.
The further the starting material moves, the more concentrated the extract becomes.
completed extraction is thus possible when the quantities of solvent and
material and their flow rates are optimized.
The process is highly efficient, requiring little time and posing no risk from high temperature.
Finally ,sufficient concentrated extract comes out at one end of the extractor
while the marc(practically free of visible solvent) falls out from the other end.

## Slide 3
Application
1) Oil is to be extracted from soya beans in a counter current stage-contact extraction apparatus, using hexane.
2) application have been concerned with the purification and separation of organic or biochemical compound.
3)application in inorganic chemistry seem to confined to separation of the radio-nuclides and a new techniques for the determination of trace elements in geological material.

## Slide 4: Supercritical Fluid Extraction (SFE)
Supercritical Fluid Extraction (SFE) is an alternative sample preparation method with general goals of reduced use of organic solvents and increase sample throughput.
The factors to consider include temperature , pressure, sample volume, analyte collection, modifier( co- solvent) addition, flow and pressure control, and restrictors.
Generally, cylindrical extraction vessels are used for SFE and their performance is good beyond any doubt.
The collection of the extracted analyte following SFE is another important step: significant analyte loss can occur during this step, leading the analyst to believe that the actual efficiency was poor.

## Slide 5
Application
SFE finds expensive application in the extraction of pesticides
Environmental samples
Food and fragrances
Essential oils
Polymers and natural product
Commercial application of the extraction process is its prohibitive capital investment

## Slide 6: Solid-phase extraction (SPE)
Solid-phase extraction (SPE) is a sample preparation process by which compounds that are dissolved or suspended in a liquid mixture are separated from other compounds in the mixture according to their physical and chemical properties.
Analytical laboratories use solid phase extraction to concentrate and purify samples for analysis.
Solid phase extraction can be used to isolate analytes of interest from a wide variety of matrices, including urine, blood, water, beverages, soil, and animal tissue

## Slide 7
The result is that either the desired analytes of interest or undesired impurities in the sample are retained on the stationary phase.
The portion that passes through the stationary phase is collected or discarded, depending on whether it contains the desired analytes or undesired impurities.
If the portion retained on the stationary phase includes the desired analytes, they can then be removed from the stationary phase for collection in an additional step, in which the stationary phase is rinsed with an appropriate eluent.
SPE uses the affinity of solutes dissolved or suspended in a liquid (known as the mobile phase) for a solid through which the sample is passed (known as the stationary phase) to separate a mixture into desired and undesired components. .

## Slide 8
Application
Technique for extraction or purification.
Solid phase extraction procedures are used not only to extract traces of organic compound from environmental samples.
application of solid phase extraction technique in analysis of different compounds in various matrices.

## Slide 9: Microwave-assisted extraction
This thermal effect is practically instantaneous at the molecular level but limited to a small area and depth near the surface of the material.
Microwave radiation interacts with dipole of polar and polarizable materials.
The couple forces of electric and magnetic components change
direction rapidly. Polar molecules try to orient in the changing field direction and hence get heated.
In non-polar solvents without polarizable groups, the heating is poor( dielectric absorption only because of atomic and electronic polarizations). The rest of the material is heated by conduction.
Thus, large particle or agglomerates of small particles can not be heated uniformly, which is a major drawback of microwave heating.
It may be possible to use high power sources to increase the depth of penetration.
However, microwave radiation exhibits an exponential decay once inside a microwave absorbing solid.

## Slide 10
Application
Pesticide analyses
Isolation of important in pharmaceutical compounds
Extraction of virtually all compounds from all matrices.
The application of microwave assisted extraction process for isolation and extraction of phytoconstituents from plant material